## Slide 1: Shale oil and gas reservoir characterisation
Alexander Repnik
Presentation of IPGC,
2 of September 2015
Giza, Egypt

## Slide 2: Outline of the project
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
0
The initial evaluation of potential of shale oil and gas basins
1
2
3
4
5
6
7
Objectives & Project highlights
Unconventionals pore system
Shale reservoir properties (selection criteria's)
Well space unconventional reservoir characterisation
3D space unconventional reservoir characterisation
Defining completion strategy
Reserves and uncertainty analysis
8
Conclusion and future opportunities of investigation
1

## Slide 3: Objectives & Project Highlights
Objectives
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
Study approach about initial evaluation of potential shale oil and gas basins
Study unconventional pore system and reservoir properties of shale plays
Developing an integrated approach for reservoir characterisation in well space and 3D domain
Construction of integrated reservoir model for reserves and uncertainty analysis
1
2
3
4
2

## Slide 4
Unique combination of subsurface temperature conditions, pressure, amount and level of maturity of organic matter.
Low geological risks
As a result
Looking to Hunt,MMmm !
Murteree-Epsilon
Shale Formations
Permian Sedimentation
Fluvial, Marine sediments
The strong influence of diagenesis on the mineral composition
The high thermal gradient
Overpressure
Depth: 2500-3000 m
Temperature: ~ 150-200 ° C
Shale Thickness > 45 m
Average TOC 2%
High temperature and pressure leads to higher plasticity species that affects the determination of horizontal wells
1
2
3
4
5
6
Preliminary geologic and reservoir characterization of shale basins and formation(s)
Evaluation of the areal extent of the shale formation(s)
Defining the prospective area for each shale gas and shale oil formations.
Estimating the Resource
7
Estimating the Technically Recoverable Resource
An initial evaluation of potential of shale oil and gas basins
The selection of region for future evaluation based on strategy of company and market gsituation
Recoverable factors
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
3

## Slide 5
The unconventionals pore system
Composite system
Integrain pore system
Hydrocarbons
Processes of maturation of TOC
Opened pores by mineralization
Deposition
influence
Pores are too small
Post deposition influence
Not connection
Fracturing are need
to produced oil and gas
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
4

## Slide 6
Description of shale play properties
Shale Reservoir Properties
Vitrinite reflectance
Total Organic Carbon
T max
Catagenesis
Gradation
LOM
Well calculations
Basin modeling
Catagenesis modeling
>1 %
>1%
> 350 C
Middle or main
> 13
Basin modeling
> 75%
Calculation from well logs
Seismic techniques
Mineralogy
Radioactivity
Brittleness
High
Core analysis
Well logs
Most Quartz
Geological
Geochemical
Geomechanical
Shale play identification
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
5

## Slide 7
Survey:Bin 12.5 on 25,Number of Inlines 1326,Number of Crosslines 707
Post stack data
Dataset for investigation
Well 1
Well 2
Seismic survey
2 wells
Well 1: logging tools, geochemistry data
Well 2: logging tools,geochemistry data
Gamma ray
Sonic
Composite Log
Mud Log
Completion Report
Time-Depth data
Seismic/Sonic Calibration
Gamma ray
Density
Sonic
Deep Resistivity
Spontaneous Potential
Composite Log
Mud Log
Completion Report
Time-Depth data
Seismic/Sonic Calibration
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
6

## Slide 8
Initial geophysical and formation evaluation study of Murteree-Epsilon formations
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
7
Depth map Epsilon Formation
Depth map Murteree Formation
Well logging study
Analysis of thin sections Murteree Formation
Quartz minerals
Organic material's

## Slide 9
Visual TOC prediction, DTvsDT_R analysis
Yes
Passey TOC estimation and calibration with lab data
Maturity analysis in according of vitrinite reflectance value analysis
Places for horizontal drilling to frac in potential zones
If DT > Dt_R
If TOC >1
Brittleness analysis
If VR0>1
Well Space Reservoir Characterisation
Completion strategy determination
Potential zone identification
If Ibr > 75 %
Rock-physics
analysis
Estimation Poisson ratio and Young modulus
Reserves estimation and uncertainty analysis
Well space unconventional reservoir characterisation
Geochemical
Geomechanical
Yes
Yes
Yes
Finding relation between geochemical, geomechanical and seismic domain
Well logging data
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
8

## Slide 10
1
2
3
4
5
6
7
Calculate LogR of all Resistivity logs
Creating Cross‐Plot LogR vs Sonic (DT)
Determine low Resistivity Shale line
Calculate new Sonic (pseudo‐sonic DtR) from Shale line [DtR=b‐m*LogR]
Overlay pseudo‐sonic (DtR) over sonic
Highlight cross over of pseudo‐sonic with DT
Calculation TOC from resistivity data
8
Correlation TOC with density data
Shale play
Non-Shale line
DtR
Well space-Geochemical: Visual TOC prediction, DTvsDT_R analysis, Passey TOC modified method-Well 1
Determination shale play
Passey TOC
Epsilon formation
Murteree formation
logR = log (RESD / RESDbase) - 2.5 * (DTC – DTCbase)
TOC = (DlogR * 10^(0.297 – 0.1688 * LOM))
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
9

## Slide 11
Well space - Geochemical: 1D Basin Modeling - Well 2
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
10
Burial History Chart
Heat Flow
SWI-Temperature
Epsilon - TOC 4 %, Type Kerogen 2
Murteree -TOC 3 %, Type Kerogen 2
Basin modeling
Vitrinite reflectance
Vitrinite reflectance changes from 1.51 to 1.57
Murteree-Epsilon Formations are dry gas zone
Source
Data

## Slide 12
Well space - Geochemical: Potential zone identification – Well 1
Overlying DT under non-shale DT
TOC > 1 %
Mature Rocks,
Vitrinite reflectance>1 %
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
11
Identification potential zones
Criteria selections

## Slide 13
Well space - Geomechanical: Poisson ratio, Young Modulus, Average Brittleness estimations
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
12
Average Brittleness
Poisson Brittleness
Young Brittleness
Poisson Ratio
Dynamic Young Modulus
Poisson Ratio

## Slide 14
Well space - Geomechanical: Places for horizontal drilling to frac in potential zones
Average brittleness >75 %
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
13
Drilling in brittle zone to frac in high potential zones
Criteria selections

## Slide 15
Well space – Rock Physics Analysis-Determination trends in geomechanical domains in according of brittleness
Murteree formation,Well-1
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
14
Epsilon formation,Well-1
Murteree formation,Well-2
Murteree formation,Well-2

## Slide 16
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
Well space – Rock Physics Analysis - Determination trends in elastic domain
15
Murteree formation,Well-1
Epsilon formation,Well-1
Murteree formation,Well-2
Murteree formation,Well-2

## Slide 17
3D generation
Modeling, vitrinite reflectance
Places for horizontal drilling to frac in potential zones
Brittleness analysis
If VR0>1
3D Space Reservoir Characterisation
Completion strategy determination
Potential zone identification
If Ibr > 75 %
Rock-physics
analysis
Estimation Poisson ratio and Young modulus
Reserves estimation and uncertainty analysis
3D space unconventional reservoir characterisation
Geochemical
Geomechanical
Yes
Yes
Well logging data
Seismic
Seismic inversion,
P-impedance
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
16

## Slide 18
3D generation modeling, vitrinite reflectance
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
17
Vitrinite map Epsilon Formation
Vitrinite map Murteree Formation
Epsilon Source TOC 4 %, Type Kerogen 2
Murteree Source TOC 3 %, Type Kerogen 2
Epsilon and Murteree surfaces
Input data:
Murteree-Epsilon Formations are dry gas zone

## Slide 19
3D space – Rock Physics Analysis-Determination relation between p-impedance and brittleness
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
18
Murteree formation,
Well-1
Epsilon formation,
Well-1

## Slide 20
3D space – Seismic inversion
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
19
Angle Gathers
RP reflectivity
RS reflectivity
ZP impedance
ZS impedance
λρ
µρρ
λρ vs. µρ crossplot
Case of presence angle gathers
Case of post-stack data
Well data
Horizons
Model
Inversion
P-impedance
Wavelet
Seismic
Epsilon(6 layers)
Murteree (Top, base) 3 layers
Well 1 and Well 2
Sonic, density logs
Check shots
Post-stack survey
P-impedance well correlation
P-impedance 2D map
Epsilon Formation

## Slide 21
3D space – Brittleness analysis
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
20
In according of rock-physics analysis, P-impedance and Brittleness have good correlation (well space), that is why based on P-impedance result brittleness was estimated.
Average brittleness well correlation
Average Brittleness 2D map
Epsilon Formation

## Slide 22
3D space – Analysis of TOC – P-impedance and Average Brittleness
21
Average Brittleness 2D map
Epsilon Formation
P-impedance 2D map
Epsilon Formation
TOC 2D map
Epsilon Formation
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion

## Slide 23
3D space – Sweet spot analysis
21
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
Reservoir Quality
Completion Quality
RQ & CQ
Good
Poor
Good
Poor
Good
Poor

## Slide 24
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
3D space – Completion strategy determination
22

## Slide 25
Integrated reservoir modeling- constriction static geological model and fluid model
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
23
Surfaces: Top Epsilon, Top Murteree, Base Murteree
Geometry: Grid increment Xinc=25 m, Yinc=25 m
Limitations: Surface boundaries
Variables | Minimal value | Base value | Maximum value
Porosity | 0,05 | 0,075 | 0,12
Net to Gross | 0,7 | 0,8 | 0,9
Gas formation volume factor | 1 | 1,1 | 1,2
Gas recovery factor | 0,2 | 0,25 | 0,3
Static geological model
Contact set for Murteree-Epsilon formations
Parameters for probability reserves estimation

## Slide 26
Reserves and uncertainty analysis – Epsilon formation
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
24
Porosity (47,32 %)
Gas recovery factor(22,14 %)
Bg(15,45 %)
Net to gross(15,09 %)
4.1
1.0
2.7
0.6
1.6
5.5
Spearman rank correlation

## Slide 27
Reserves and uncertainty analysis – Murteree formation
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
25
Porosity (46,45 %)
Gas recovery factor(29,2 %)
Spearman rank correlation
Bg (15,53 %)
Net to gross(13,83 %)
5.3
1.3
0.8
3.6
2
7.2

## Slide 28
Outline
Shale plays
Basin potential
Well space characterisation
3D space characterisation
Reserves and uncertainty
Conclusion
Conclusion
25
Studied method and made initial evaluation about basin potential
Studied difference between unconventional and conventional pores systems
The integration approach was developed which, allow making following things:
  characterize reservoir through brittle and maturity view
  identify hydrocarbons zones
  evaluate recoverable factor based on brittleness and geological complexity
  make completion strategy based on brittleness
  identify zones for horizontal drilling
  evaluate volume of proppant for fracturing
  make complex evaluation about perspective of selected formations
Future opportunities
Adding investigation of fractures geometries by seismic interpretation
Adding seismofacies description and correlation them with TOC and brittleness
Trying to combine multifocusing method and fracture geometry description

## Slide 29
Shale oil and gas reservoir characterisation
Thank you !
!شكر
Giza, Egypt, 2 September 2015